PETR 5313: CRN 38950, Fall 2017
Numerical Application in Petroleum Engineering,
Lesson 08: Interpolation, Extrapolation, and Integration
Ekarit Panacharoensawad, PhD
Terry Fuller Petroleum Engineering Research Building Room 236
ekarit.panacharoensawad@ttu.edu
Copyleft: No rights reserved
Cite as: Panacharoensawad, E. (2017) "Numerical application in petroleum engineering, Lesson 08: Interpolation - Extrapolation", presentation slide for Texas Tech PETR 5313 Fall 2017

---
Outline
  1. Interpolation
  2. Extrapolation
    1. 1D data
    2. 2D data
    3. Linear
    4. Cubic spline

---
Linear Interpolation
Draw a straight line connected two dots A and B to tell the f(x) value based on the give x value.
x\in[A,B]
\frac{y-y_0}{x-x_0} = \frac{y_1-y_0}{x_1-x_0}
y = y_0 + (y_1 - y_0)\frac{x-x_0}{x_1-x_0}
y=\frac{x_1-x}{x_1-x_0}y_0+\frac{x-x_0}{x_1-x_0}y_1

---
Method for interpolation
1. Given data:
2. Target: y value at xt (val)
3. Manual
  1. Need to find xi and xi+1 that xt stays in between
    1. idx = np.abs(x-val).argmin()
      1. x is list, .argmin() find the index where minimum value occur
    2. idx2 = np.searchsorted(x, val) – 1
      1. This give the index on the left boundary
\boldsymbol{x} = [x_1, x_2, \dots, x_n]
\boldsymbol{y} = [y_1, y_2, \dots, y_n]

---
Method for interpolation
1. Automatic Function: numpy.interp
2. np.interp(val,x,y)
  1. This is to get y at x value equal to val
3. val can be list of values too
  1. This does interpolation several times

---
Linear Extrapolation
1. Extend a straight line outside the domain to get the value of y at an interested x
  1. Equation is the same as linear equation
2. Manual method
  1. Need to find if extrapolation is on left or right side of the domain
3. Automatic
  1. from scipy import interpolate
  2. Lin_inter = interpolate.interp1d(x,y,kind='linear'
    ,fill_value='extrapolate')
  3. y_sp = Lin_inter(val)

---
Interpolation for 2D data: Use Scipy
1. model = interpolate.interp2d(x = T_in,
2. y = P_in, z = Mu_in)
3. val = (70,3000)
4. z_pred = model(*val)
5. P_in.shape gives (11,)
6. T_in.shape gives (7,)
7. Mu_in.shape gives (11, 7)

---
Interpolation for 2D data: Manual
1. From (z,T) = (109.7, 66.7) and (93.5, 75) at P = 2550
  1. Find z at T = 70.0 (target) by linear interpolation
2. From (z,T) = (97.5, 66.7) and (81.2, 75) at P = 3040
  1. Find z at T = 70.0 (target) by linear interpolation
3. From (z,P) = (103.2, 2550) and (90.978, 3040) at T = 70
  1. Find z at P = 3000 (target) by linear interpolation
\begin{bmatrix} & \text{T\_in[2] = 66.7} & \text{x\_target = 70.0} & \text{T\_in[3] = 75.0}\\ \text{P\_in[5] = 2550.0} & 109.7 & 103.2 & 93.5\\ \text{y\_target = 3000} & & 91.9776 &\\ \text{P\_in[6] = 3040.0} & 97.5 & 90.978 & 81.2 \end{bmatrix}

---
Simple Cubic Spline
1. Input: Slope + coordinate of 2 points
  1. (x1, y1), (x2, y2)
  2. Slope at (x1, y1) and (x2, y2)
2. Output:
  1. Curve that pass those 2 points and have the specified slope

---
Simple Cubic Spline: Curve fitting equation
1. q is the cubic spline prediction
2. k is the slope
q = (1-t)y_1 + t y_2 + t(1-t)(a(1-t)+bt)
t=\frac{x-x_1}{x_2-x_1}
a = k_1(x_2-x_1)-(y_2 - y_1)
b = -k_2(x_2 - x_1) + (y_2 - y_1)

---
Simple Cubic Spline: Example
1. For
4. Find the interpolation / extrapolation curve from cubic spline
x = np.linspace(-1,2,100)
t = (x-x1)/(x2-x1)
a = k1*(x2 - x1) - (y2 - y1)
b = -k2*(x2 - x1) + (y2 - y1)
q = (1 - t)*y1 + t*y2 + t*(1 - t)*(a*(1 - t) + b*t)
x1 = 0 \qquad\quad x2 = 1
y1 = 0 \qquad\quad y2 = 0
f'(x1) = 1 \qquad f'(x2) = 1

---
Simple Cubic Spline for Various Cases
1. For k2 in [-2, -1, 0, 1, 2], we have
2. Cubic spline adjusts the interpolation curve according to the specified slope

---
Cubic Spline for Multiple Points
1. Advantages of using cubic spline
  1. Cubic spline can approximate the slope between points accurately (in addition to the function value)
2. Use Cubic spline when trying to approximate the slope of function based on the samples of function values
3. Output properties
  1. q(x), q’(x), and q’’(x) are piecewise continuous functions!

---
Cubic Spline for Multiple Points: Natural B.C.
  1. When we have many points, we typically do not know the slope at each point.
  2. To use cubic spline without knowing the slope, the boundary condition on each end should be specified
  3. One simple and powerful assumption is that q’’(x0) and q’’(xn) = 0
    1. This is called “natural boundary condition”
    2. This mean that the curves are just straight at both ends location

---
Cubic Spline for Multiple Points: Example
1. Cubic Spline solution was done by not knowing the function used to generate the data points
Before cubic spline interpolation
After cubic spline interpolation

---
Cubic Spline for Multiple Points: Example
Slope from cubic spline is comparable to the analytical solution

---
Cubic Spline for Multiple Points: Example
Integration of the approximation function is also close to the analytical solution of the original equation
\int_1^xf(x) dx

---
Cubic Spline for Multiple Points: Calculation Steps
  1. Solve for slope at each points by assume the second derivative to be zero for the end points (natural B.C.)
  2. Once the slopes are obtained, use Simple cubic spline approach to get the interpolation value in each interval
2. Variable definition
  1. k = slope (to be calculated)
  2. x[i] = given x-coordinate of the point i
  3. y[i] = given y-coordinate of the point i

---
Cubic Spline: Slope Calculation
  1. Solve system of linear equations to get all k
for i = 0
for i = 1 to n-1
for i = n
B_{0}k_{0} + C_{0} k_{1} = D_{0} \qquad\qquad\quad\:
A_{i}k_{i-1} + B_{i}k_{i} + C_{i} k_{i+1} = D_{i} \qquad
A_{n}k_{n-1} + B_{n}k_{n}= D_{n} \qquad\qquad\:\:
\begin{bmatrix} B_0 & C_0 \\ A_1 & B_1 & C_1 \\ & \ddots & \ddots & \ddots \\ & & \ddots & \ddots & \ddots \\ & & & A_{n-1} & B_{n-1} & C_{n-1}\\ & & & & A_n & B_n \end{bmatrix} \begin{bmatrix} k_0\\ k_1\\ k_2\\ \vdots\\ k_{n-1}\\ k_{n} \end{bmatrix} = \begin{bmatrix} D_0\\ D_1\\ D_2\\ \vdots\\ D_{n-1}\\ D_{n} \end{bmatrix}

---
Cubic Spline: Slope Calculation...
1. Derivation: https://en.wikipedia.org/wiki/Spline_interpolation
\begin{align*} 2(x_1-x_0)\:k_0 + (x_1-x_0)\:k_1 & = 3 (y_1-y_0) \\ \frac {k_{i-1}}{x_i-x_{i-1}} + \left(\frac {1}{x_i-x_{i-1}}+ \frac {1}{{x_{i+1}-x_i}}\right) 2k_i+ \frac {k_{i+1}}{{x_{i+1}-x_i}} & = \\ 3 \left(\frac {y_i - y_{i-1}}{{(x_i-x_{i-1})}^2}+\frac {y_{i+1} - y_i}{{(x_{i+1}-x_i)}^2}\right)\\ (x_n-x_{n-1})\:k_{n-1} + 2(x_n-x_{n-1})\:k_n & = 3 (y_n-y_{n-1}) \end{align*}

---
Cubic Spline: Slope Calculation...
Coefficient for system of linear equation
\begin{align*}A_i & = \frac {1}{x_i-x_{i-1}}\\ B_i & = 2 \left(\frac {1}{x_i-x_{i-1}}+ \frac {1}{{x_{i+1}-x_i}}\right)\\ C_i & = \frac {1}{{x_{i+1}-x_i}}\\ D_i & = 3 \left(\frac {y_i - y_{i-1}}{{(x_i-x_{i-1})}^2}+\frac {y_{i+1} - y_i}{{(x_{i+1}-x_i)}^2}\right) \end{align*}

---
Cubic Spline: Solving Manually
B0 = 2*(x[1]-x[0])
C0 = x[1]-x[0]
D0 = 3*(y[1]-y[0])
Ai = [1.0/(x[i]-x[i-1]) for i in range(1,len(x)-1)]
Bi = [2 * (1.0/(x[i]-x[i-1]) + 1/(x[i+1]-x[i])) for i in range(1,len(x)-1)]
Ci = [1.0/(x[i+1]-x[i]) for i in range(1,len(x)-1)]
Di = [3*((y[i]-y[i-1])/(x[i]-x[i-1])**2 + (y[i+1]-y[i])/(x[i+1]-x[i])**2)
      for i in range(1,len(x)-1)]
n = len(x) - 1 # the index is from 0 to n-1, not to n
An = x[n]-x[n-1]
Bn = 2*(x[n]-x[n-1])
Dn = 3*(y[n]-y[n-1])
AA = Ai+[An] # + operation for list is concatenation (similar to .append)
BB = [B0] + Bi + [Bn]
CC = [C0] + Ci
DD = [D0] + Di + [Dn]
CSpline = sp.sparse.diags(diagonals=[BB,AA,CC], offsets=[0,-1,1])

---
Cubic Spline: Using automatic function
1. model = sp.interpolate.CubicSpline(x,y,bc_type='natural')
2. y_pred = model(np.linspace(1,10,100))
3. Scipy automatic function is shorter and it is doing the same things with the manual implementation

---
Calculate Slope / Integrating Area from Cubic Spline
1. Get prediction of y, y’, and y’’
  1. y_pred = model(np.linspace(1,10,1000))
  2. y_slope_pred = model(np.linspace(1,10,1000),nu=1)
  3. y_slope2_pred = model(np.linspace(1,10,1000),nu=2)
2. Get integration result
  1. x_inte = np.linspace(1,10,101)
  2. y_inte = [model.integrate(1,i) for i in x_inte]